# Localizing a SCUBA Diver Using Active Sonar
Richard Guilmain and Nabin Sharma
Georgia Tech
# 1. Problem Description
The threat of an underwater terrorist attack is a concern of the maritime industry, port law enforcement, and luxury and high-profile vessel owners alike. Prevention of such attacks needs to start with the reliable detection of sub-surface threats such as SCUBA and closed-circuit re-breather (CCR) divers. Because these threats are below the water’s surface, traditional detection methods such as radar and visual surveillance are unavailable, making active sonar technology the most effective approach to date. However, because of the inherent noise of the underwater acoustic environment—often rife with mechanical noise, reflective debris, and environmental marine activity—current sonar methods are often inconsistent. Better processing methods are required to manage this low signal-to-noise ratio while still localizing the range and bearing of threatening divers at tactically significant ranges.
Given the noisy range and bearing measurements from an active sonar receiver, the goal is to estimate the range of the target to the sensor, the bearing of the target to the sensor, and the heading direction that the target is moving in. Due to the relatively unstable propagation environment, underwater targets like SCUBA divers might not be detected at all measurement steps even if relatively noisier measurements are accepted as valid ones. This leads to the requirement of more robust localization schemes so that we don't lose valid targets.

Figure 1: Basic graphical representation of a typical diver localization scenario. Sonar measurements provide the range (r) of the target (or diver) from the sonar sensor and bearing (ө) from the sonar sensor axis represented by dashed line. The angular span of the sensor field-of-view is 90 degrees.

Figure 2: Block diagram of the active sonar receiver used to obtain diver measurements.
# 2. Sensor and Measurements
Figure 1 shows a typical diver localization scenario. The bottom center point of the sector in Figure 1 represents the location of an active sonar sensor located either on a fixed platform (such as a pier) or on a rotating and translating platform (such as an anchored vessel). The sonar system is responsible for providing measurements to our diver localization algorithm. The sonar transmits an acoustic pulse every 1.3 seconds and listens for echo returns via a multichannel receive array. Figure 2 shows the signal and data processing block diagram of the sonar system. Data received from the sensor array passes through several signal processing modules, including a lowpass filter and a digital downconverter, before it gets beamformed. During beamforming, the sonar software combines the signals from all of the receiving array channels in a controlled manner so that the time delays experienced by the sonar echoes entering the different receive channels are equalized for desired directions along which sonars want to look for targets. This effectively increases the receiver gain in the desired directions and thus helps to get better diver or target measurements.

Figure 3: A representative sonar sector. As shown in Figure 1, the sonar field-of-view is 90 degrees and the maximum range is 500 meters. The relatively stronger patch at around 0 degrees and 450 meters is the diver.

As shown in Figure 1, we set the sonar's beamformer to look for 45 degrees on both sides of the sonar's axis. This sets the sonar's angular field-of-view to be 90 degrees. The maximum range of the sonar is 500 meters. The angular field of view and the maximum detection range of the sonar define the sonar sector as shown in Figure 1 - the only area in front of sonar which can be scanned for targets. Figure 3 shows a sector generated using the range and angular settings as specified in Figure 1. The relatively strong patch around 0 degrees and 450 meters is a SCUBA diver swimming towards the sonar. It is evident from Figure 3 that the sector data coming out of the beamformer can be quite noisy depending on the conditions of the water and the surrounding environment. As such, we have to accept some level of false detections to also pick up on true measurements of the diver. This leads to the requirement of a probabilistic localization algorithm if we want to detect the diver with a high level of confidence.

The detector in Figure 1 tries to minimize the effects of noise and false detections as much as possible without losing the true target measurements. To do this, it implements ping-to-ping exponential smoothing and background subtraction algorithms to provide relatively cleaner moving target measurements to the localization algorithm. The targets that are of most importance are the ones moving towards the ship or sonar. Therefore, the detector is tuned to detect targets that are moving radially towards the sonar sensor more effectively than targets moving otherwise.

# 3. Hypothesis and Project Approach
(We want to explain the basic working and assumptions of particle filter)